## Slide 1: RCANN – A ReConfigurable Artificial Neural Network for Iris Flower Classification
Matthew Griessler and Nick Landy

## Slide 2: RCANN
Project Description:
RCANN is a configurable neural network implemented with reconfigurable computing principles on a ZYNC SoC
Project Demonstration:
RCANN is configured for the Iris flower dataset and the functionality is demonstrated. The Iris flower dataset is a dataset commonly used in classification algorithm development
From left to right: Iris setosa, Iris versicolor, Iris virginica

## Slide 3: What is a Neural Network
Examples of Common Datasets |  |  | 
Dataset | Input Layer | Hidden Layer | Output Layer
MNIST Handwriting | 784 | 15 | 10
Iris flower | 4 | 15 | 3
Input Layer
Hidden Layer
Output Layer

## Slide 4: What is a Neural Network
Examples of Common Datasets |  |  | 
Dataset | Input Layer | Hidden Layer | Output Layer
MNIST Handwriting | 784 | 15 | 10
Iris flower | 4 | 15 | 3
Input Layer
Hidden Layer
Output Layer
Why three layers??

## Slide 5: Neural Network - Node
It all starts with the node

## Slide 6: Neural Network – Activation Function
Sigmoid function
Elliot Sigmoid function

## Slide 7: Neural Network – Forward Pass
Process layers in order: first layer, hidden layer, output layer
Within a layer, nodes can be processed in parallel
Each node requires a multiply, accumulate, and activation function evaluation to get an output

## Slide 8: Neural Network – Forward Pass
All weights and thresholds (or biases) start out randomized.
The network self-adjusts the weights and thresholds during training to increase accuracy of network.
RCANN is designed for cross-validation training.

## Slide 9: Neural Network - Backpropagation
General idea: evaluate a cost function:
Then minimize cost function by adjusting weights and biases.
This is done via the backpropagation algorithm

## Slide 10: Neural Network - Backpropagation
 | Equation | Description
BP1 |  | Solves for the error delta in the last layer
BP2 |  | Solves for the error delta in layer l based on the error in layer l+1
BP3 |  | Solves for the component of the error due to the bias
BP4 |  | Solves for the component of the error due to the weights
 | Equation | Description
BP1 |  | Solves for the error delta in the last layer
BP2 |  | Solves for the error delta in layer l based on the error in layer l+1
BP3 |  | Solves for the component of the error due to the bias
BP4 |  | Solves for the component of the error due to the weights

## Slide 11: Neural Network - Procedure
Phase of Operation | Forward pass | Check Answer | Backpropagation
Training | Yes | Yes | Yes
Verification | Yes | Yes | No
Evaluation | Yes | No | No
Neural network Use Procedure
Train for one epoch
Run verification
If performance is above threshold for accuracy (in our case 80%), go to step 4, otherwise, go back to step 1
Neural network is now ready for use with data where the answer isn’t known

## Slide 12: Have we met our Requirements?
Req # | Requirement Description
General Requirements | 
G1 | Implement a neural network on an FPGA
G2 | Interface between FPGA and host computer
G3 | Demonstrate a speedup from implementation
G4 | Support training, verification, and evaluation
G5 | Support epoch and batch processing
Neural Network Requirements | 
N1 | Three layer network
N2 | Each layer can be configured with generic number of nodes
N3 | Implement forward pass, verification, and backpropagation
Forward Pass Requirements | 
F1 | Support pipe-lined and non-pipelined operation
F2 | Implement Elliot Sigmoid function for activation function
F3 | Take input from double buffered input memory
F4 | Put output into double buffered output memory
Verification Requirements | 
V1 | Check output against expected answer stored in double buffered memory
Backpropagation Requirements | 
B1 | Implement backpropagation equation BP1
B2 | Implement backpropagation equation BP2
B3 | Implement backpropagation equation BP3
B4 | Implement backpropagation equation BP4
B5 | Update node layer-layer weights
B6 | Update node biases

## Slide 13
Implementation – Big Picture

## Slide 14: Datapath Operation

## Slide 15: Configure NN
1: Turn on back propagation (training)
0: Turn off back propagation (testing)
The number of epochs to train for.
Number of data per epoch
Loads weights and biases into NN
Input Data

## Slide 16: Test Flowchart

## Slide 17: Train Flowchart
Trains for a number of epochs specified by Num Epochs control signal

## Slide 18: Neural Network Implementation

## Slide 19: Block Diagram (Neural Network Datpath)
D
Q
D
Q
Input[3:0]
D
Q
D
Q
a1[3:0]
Clk
Cntrl
Clk
Cntrl
Clk
Cntrl
W2[3:0][3:0]
b2[3:0]
a2[3:0]
W3[2:0][3:0]
b3[2:0]
a3[2:0]
MAC
a1[3:0]
W2[0][3:0]
...
b2[0]
σ
a2[0]
σ'2[0]
MAC
a1[3:0]
W2[1][3:0]
σ
a2[1]
σ'2[1]
MAC
a2[3:0]
W3[0][3:0]
σ
a3[0]
σ'3[0]
MAC
a2[3:0]
W3[1][3:0]
σ
a3[1]
σ'3[1]
MAC
a2[3:0]
W3[2][3:0]
σ
a3[2]
σ'3[2]
σ'2[3:0]
σ'3[2:0]
b2[1]
b3[1]
b3[0]
b3[2]

## Slide 20: Block Diagram (Parameters: Error Calc.)
Clk
Cntrl
a3[2:0]
σ'3[2:0]
y[2:0]
a3[0]
y[0]
σ'3[0]
-
+
*
δ3[0]
a3[1]
y[1]
σ'3[1]
-
+
*
δ3[1]
a3[2]
y[2]
σ'3[2]
-
+
*
δ3[2]
δ3[2:0]
Clk
Cntrl
σ'2[14:0]
δ2[14:0]
MAC
W3[2:0][14:0]
δ3[2:0]
δ3[2:0]
W3[2:0][0]
*
σ'2[0]
δ2[0]
MAC
δ3[2:0]
W3[2:0][1]
*
σ'2[1]
δ2[1]
...

## Slide 21: Block Diagram (Parameters: Updates)
Clk
Cntrl
*
*
D
Q
δ2[13]
a1[2]
-n
+
w[2][13]
*
D
Q
δ2[13]
-n
+
b[1][13]
...
...
a1[2:0]
δ3[14:0]
n
W2[14:0][3:0]
b2[14:0]

## Slide 22: Demo: Testbench Simulations

## Slide 24: Example Data Samples (from IRIS Data Set)
Stem Length = 4.8
Stem Width = 3.4
Petal Length = 1.9
Petal Width = 0.2
Flower Type = 0
Stem Length = 6.1
Stem Width = 2.8
Petal Length = 4.7
Petal Width = 1.2
Flower Type = 1
Stem Length = 6.5
Stem Width = 3.0
Petal Length = 5.8
Petal Width = 2.2
Flower Type = 2

## Slide 33: Performance

## Slide 34: Performance

## Slide 35: Performance

## Slide 36: Utilization

## Slide 37: Timing

## Slide 38: Other Notes
Utilized (8.8) signed fixed point library to limit resource usage
Used array data types to help organize large matrix and vector operations
Hierarchical Design (23 design files in total)
Large amount of parameterization (learning rate, epoch size, number of epochs, layer sizes, data widths for signed fixed point data, pipelining/non-pipelining)
Exhibits good speedup for resource intensive operations (especially for forward pass where we use pipelining)