## Slide 1: RCANN – A ReConfigurable Artificial Neural Network for Iris Flower Classification
Matthew Griessler and Nick Landy

## Slide 2: Agenda
Change from Proposal
Application Description
Implementation Requirements
Implementation Design
Project Status
Testing Plan
Moving Forward

## Slide 3: What is a Neural Network
Dataset | Input Layer | Hidden Layer | Output Layer
MNIST Handwriting | 784 | 15 | 10
Iris flower | 4 | 15 | 3
Input Layer
Hidden Layer
Output Layer

## Slide 4: Changes from proposal
The MNIST design requires more MACs than available
We switched to a much simpler dataset, the iris data set
Dataset | Input Layer | Hidden Layer | Output Layer
MNIST Handwriting | 784 | 15 | 10
Iris flower | 4 | 15 | 3
Implications of changing datasets
Structure: Same
Required resources: Decreases

## Slide 5: Neural Network - Node
It all starts with the node

## Slide 6: Neural Network – Activation Function
Sigmoid function
Elliot Sigmoid function

## Slide 7: Neural Network - Procedure
Phase of Operation | Forward pass | Check Answer | Backpropagation
Training | Yes | Yes | Yes
Verification | Yes | No | No
Evaluation | Yes | No | No
Neural network Use Procedure
Train for one epoch
Run verification
If performance is above threshold for accuracy (in our case 80%), go to step 4, otherwise, go back to step 1
Neural network is now ready for use with data where the answer isn’t known

## Slide 8: Neural Network – Forward Pass
Process layers in order: first layer, hidden layer, output layer
Within a layer, nodes can be processed in parallel
Each node requires a multiply, accumulate, and activation function evaluation to get an output

## Slide 9: Neural Network - Backpropagation
General idea: evaluate a cost function:
Then minimize cost function by adjusting weights and biases.
This is done via the backpropagation algorithm

## Slide 10: Neural Network - Backpropagation
 | Equation | Description
BP1 |  | Solves for the error delta in the last layer
BP2 |  | Solves for the error delta in layer l based on the error in layer l+1
BP3 |  | Solves for the component of the error due to the bias
BP4 |  | Solves for the component of the error due to the weights
 | Equation | Description
BP1 |  | Solves for the error delta in the last layer
BP2 |  | Solves for the error delta in layer l based on the error in layer l+1
BP3 |  | Solves for the component of the error due to the bias
BP4 |  | Solves for the component of the error due to the weights

## Slide 11: Implementation Requirements
Req # | Requirement Description
General Requirements | 
G1 | Implement a neural network on an FPGA
G2 | Interface between FPGA and host computer
G3 | Demonstrate a speedup from implementation
G4 | Support training, verification, and evaluation
G5 | Support epoch and batch processing
Neural Network Requirements | 
N1 | Three layer network
N2 | Each layer can be configured with generic number of nodes
N3 | Implement forward pass, verification, and backpropagation
Forward Pass Requirements | 
F1 | Support pipe-lined and non-pipelined operation
F2 | Implement Elliot Sigmoid function for activation function
F3 | Take input from double buffered input memory
F4 | Put output into double buffered output memory
Verification Requirements | 
V1 | Check output against expected answer stored in double buffered memory
Backpropagation Requirements | 
B1 | Implement backpropagation equation BP1
B2 | Implement backpropagation equation BP2
B3 | Implement backpropagation equation BP3
B4 | Implement backpropagation equation BP4
B5 | Update node layer-layer weights
B6 | Update node biases

## Slide 12: Implementation Design

## Slide 13: Project Status

## Slide 14: Testing Plan

## Slide 15: Moving Forward